## Slide 1: The Physical Layer
Notes: Video Module 3-01

## Slide 2
Overview
Objectives
  Learn and understand the physical layer in the OSI Reference Model
  Learn and understand the effects of a medium on a signal.
  Learn and understand the techniques to mitigate the above effects.
  Learn and understand the relationships between bitrate, transmission time, propagation time.
Requirements
  Know the OSI Reference Model
  Read Sections 2.1.1 and 2.1.3
  Read Section 2.3.1
  Read 2.5.1-2.5.3
  Read 2.4.4

## Slide 3: Introduction
Physical layer in the OSI Reference model
Fundamental (adverse) effects of a medium on the signal
  attenuation
  delay
  unfairness (signal of different frequencies are treated differently)
Fourier Theorem
Maximum Data Rate of a Channel
Read Sections 2.1.1-2.1.3

## Slide 4: OSI Reference Model
Application
Application
Presentation
Presentation
Interface
Interface
Session
Session
Interface
Interface
Transport
Transport
Interface
Interface
Protocol
Protocol
Protocol
Protocol
Interface
Interface
Interface
Interface
Network
Network
Data Link
Interface
Interface
Phys.
Phys
Interface
Interface
Interface
Interface
Phys.
Phys
Network
Network
User/Client
User/Server
Data Link
Data Link
Data Link

## Slide 5: Physical Layer
Offers service to data link layer
Transmission of raw bits
Deals with:
  Electrical specs
  Mechanical specs
Tries to deliver as many bits as possible per unit time without corruption or loss.

## Slide 6: (Adverse) Impact/Effect of a Medium on a Signal
A medium :
  attenuates a signal
  Delays a signal
  Is unfair to signals using different frequencies:
    Signals of different frequencies experience DIFFERENT attenuations and delays
  The unfairness produces DISTORSION, making it hard to recognize the original sent signal
In short, a medium is a kind of …..
……. a washing machine


## Slide 7: Impact of a Washing Machine on a Garment
A Washing machine:
  Shrinks (attenuates!) a garment
  Delays a garment
  Is unfair to garments using different fabrics
    Washing with hot water shrinks wool much more than denim (fabric for jeans)
  There is a limit on the capacity of a washing machine.

## Slide 8: No More Laundry Talks …....
Let us formalize these ideas.

## Slide 9: Fundamental Properties
Section 2.1.1: (Fourier) any periodical signal with frequency f is a superposition (sum) cosine and sine waves of different frequencies
Section 2.1.2: Real media affect (attenuates, delays) different frequency signals differently
Section 2.1.3: there is a theoretical limit on the maximal data rate on a channel
  Nyquist limit (noiseless channel) is bps
    where B is the bandwidth, and V is the valence, i.e., the size of the vocabulary (number of of possible symbols).
    example: my vocabulary is made of {0, 1, 2, 3}. Then V = 4
  Shannon limit (noisy) is bps
    where B is the bandwith, S is the power of the signal, and N the power of noise,
    Pay attention: S/N is often expressed as SNR, i.e., the Signal to Noise ratio in Db (decibel) where
    )
    Example: if SNR = 20 Db, then solving will yield ) will yield 100

## Slide 10: Mitigating the Consequences of Fourier Theorem
Consequences of Fourier Theorem
  Baseband transmission
  Why do we need modems for long distance communications?
  MODEM (MOdulates – DEModulate
Read Sections 2.2.1-2.2.3 and 2.2.5 (skip 2.2.4)
Notes: Video Module 3-02

## Slide 11: Consequences of Fourier
Square signals (baseband transmission) are badly affected by channels
  because square signals are a mix of signals of different frequencies
  Recall: signals of different frequencies are attenuated and delayed differently
   square signals are distorted.
There is only limited ways to increase data rate and fight attenuation, delay, and discrimination (frequency unfairness) (2.5.1)
  Use better media:
    twisted pair,
    coaxial cable,
    fiber
  Symbol rate (baud rate) versus bit rate:
    If the vocabulary consists of 2n symbols, Bit Rate = n Baud Rate
  Use better encoding schemes:
    NRZ,
    NRZI,
    Manchester

## Slide 12: Better Encoding Schemes for Baseband Transmission
Encoding schemes:
  NRZ,
  NRZI,
  Manchester

## Slide 13: Better Encoding Schemes for Baseband Transmission
Encoding schemes:
  NRZ,
  NRZI,
  Manchester

## Slide 14: Better Media
Guided Transmission Media
  Magnetic Media (2.2.1)
  Twisted pairs (2.2.2)
  Coaxial cable (2.2.3)
  Fiber optics (2.2.5)
Wireless Transmission

## Slide 15: Better Media
Guided Transmission Media
  Magnetic Media (2.2.1)
  Twisted pairs (2.2.2)
  Coaxial cable (2.2.3)
  Fiber optics (2.2.5)
Wireless Transmission

## Slide 16: Baseband Cannot Be Used Long Distances Modulation
=== Modulation such that a signal is made of a limited number of frequencies (2.5.2).
  ASK (Amplitude Shift Keying), FSK (Frequency SK), PSK (Phase SK)
ASK
FSK
PSK

## Slide 17: Baseband Cannot Go On Long Distances Modulation
=== Modulation such that a signal is made of a limited number of frequencies (2.5.2).
  ASK (Amplitude Shift Keying), FSK (Frequency SK), PSK (Phase SK)
ASK
FSK
PSK

## Slide 18: Consequences of Maximal Capacity
Consequences of the Capacity Limit (bit rates)
  Nyquist/Shannon Limits
  How to share the channel?
Read Sections 2.5.1, 2.5.3-2.5.5
Notes: Video Module 3-03

## Slide 19: Consequences of the Capacity Limit
Multiple users must share the medium
  How to share?
    Frequency division multiplexing (FDM) (2.5.3)
    Time division multiplexing (TDM) (Section 2.5.4)
    Code Division Multiplexing (2.5.5)

## Slide 20: Frequency Division Multiplexing (FDM)
A medium is divided in multiple channels
Each channel is carried on different frequency bands.

## Slide 21: Frequency Division Multiplexing (FDM)
A medium is divided in multiple channels
Each channel is carried on different frequency bands.

## Slide 22: Time Division Multiplexing (TDM)
A medium is used in turns (round robin) by multiple users.

## Slide 23: Time Division Multiplexing (TDM)
A medium is used in turns (round robin) by multiple users.

## Slide 24: Code Division Multiplexing Access (CDMA)
Different stations A and B are assigned codes (chip sequences) a and b for each bit such that a and b are orthogonal  a. b = 0
  Example:
    To send 0 (resp.1) using the chip a, Station A sends –a (resp. a).
    To send 0 (resp.1) using the chip b, Station B sends –b (resp. b).
    Suppose that Station A sends 1 (a) and Station B sends 1 (b). A receiver will see the superposition of both signals, i.e. S = a + b.
    How can a receiver know what Station A sent?
    To extract a from S, a receiver must multiply S by ….
    Suppose that Station A sends 0 (-a) and Station B sends 1 (b). A receiver will see the superposition of both signals, i.e. S = -a + b.
    How can a receiver know what Station A sent?
    To extract a from S, a receiver must multiply S by ….

## Slide 25: Code Division Multiplexing Access (CDMA)
Different stations A and B are assigned codes (chip sequences) a and b for each bit such that a and b are orthogonal  a. b = 0
  Example:
    To send 0 (resp.1) using the chip a, Station A sends –a (resp. a).
    To send 0 (resp.1) using the chip b, Station B sends –b (resp. b).
    Suppose that Station A sends 1 (a) and Station B sends 1 (b). A receiver will see the superposition of both signals, i.e. S = a + b.
    How can a receiver know what Station A sent?
    To extract a from S, a receiver must multiply S by ….
    Suppose that Station A sends 0 (-a) and Station B sends 1 (b). A receiver will see the superposition of both signals, i.e. S = -a + b.
    How can a receiver know what Station A sent?
    To extract a from S, a receiver must multiply S by ….

## Slide 26: Delay
Delay components
  Transmission time
  Propagation time
  Queueing delay
Notes: Video Module 3-04

## Slide 27: Delay
Sender
Receiver
Bandwidth (bit rate)
Propagation Time
Travel Time
Propagation Time (Tp)
Loading Time
Transmission Time
Transmission Time
Speed of signal)
Upper Layer Feeder
Feeding rate larger than bit rate
Queueing Time

## Slide 28: Delay (Cont’d)
Total delay T = Queueing Time + Time to load + Travel Time
  T = Queueing Time + Transmission Time + Propagation Time
  = + +
Let S be the size of a frame (packet) and br be the bit rate.
The Transmission Time (Time to put bits on the medium)
The Propagation Time
  where is the distance and is the speed of the signal on a medium. (On copper wires, v = 2/3 c where c is the speed of light)
The Queueing Time is often random. For now, we will consider it 0.

## Slide 29: Delay : units, constants, conventions (to know)…
The speed of light c is 299,792,458 m/s. Throughout this course use this approximation: c = 3 108 m/s = 3 105 km/s.
The speed on copper is about 2/3 the speed of light (2 105 km/s )
The bit rate is often expressed in Kbits/s (Kilobit = 103 bits), Mbits/s (Megabit = 106 bits), or Gbits/s (Gigabit = 109 bits).
Important, when expressing a bit rate
  Kilo = 103
  Mega = 106
  Giga = 109
Important, when expressing data size (storage, packet size…)
  Kilo = 210
  Mega = 220
  Giga = 230
Time units
  milliseconds (ms) (10-3 s)
  microseconds (ms) (10-6 s)
  nanoseconds (ns) (10-9 s)

## Slide 30: Wrap Up
  Learn and understand the physical layer in the OSI Reference Model
  Learn and understand the effects of a medium on a signal.
  Learn and understand the techniques to mitigate the above effects.
  Learn and understand the relationships between bit rate, transmission time, propagation time.
Notes: Video Module 3-05