## Slide 1: Network Layer
Notes: Video Module 5-01

## Slide 2
Overview
Objectives
Get familiar with the Network Layer
Learn and understand Routing Policies (algorithms and protocols)
Learn how to Update Routing Tables (Routing policy)
Learn about the routing mechanism (IP) for Routing over the Internet
Learn about some IP helpers (IP)
Requirements
Read Intro, 5.1.1, 5.1.2, 5.1.3,
Read 5.2 Intro, Skim 5.2.1, Skim 5.2.2, Skim 5.2.3,
Read 5.2.4, Read 5.2.5,
Skim 5.5,
Read 5.6 up to 5.6.2
Read 5.6.4

## Slide 3: Introduction
The network layer in the OSI Reference model
Functions/Services of the network Layer
Connectionless and connection oriented
Read Introduction and Sections 5.1.1-5.1.3
Notes: Video Module 7-01

## Slide 4
Where in the OSI Reference Model ?
Transport Layer
Network Layer
Link Layer
Physical Layer
Session Layer

## Slide 5: Fundamental Functions of a Network Layer
Neat interface for the transport layer
Addressing
Routing
Congestion control
  Some network protocols provide congestion control

## Slide 6: Network Layer Protocols : two families
Connectionless
  Each piece of information (message) is sent as an independent entity. No state information is kept on hosts, routers, or intermediary L3 switches.
Connection oriented
  There exists a virtual circuit over which all pieces of information (messages) will transit. Intermediary nodes keep a state about the circuit.

## Slide 7: Connectionless vs Connection-oriented
Circuit setup
Addressing
State information
Routing
Effect of routing failures
Congestion control

## Slide 8: Routing
Routing policy:
  updates the routing table
Routing mechanism:
  decides how to route a packet depending on some policy (i.e, chooses the output line)
Routing
table
modifies
reads
Quite elementary

## Slide 9: Routing Policy Algorithms
How to update the routing tables?
  Routing algorithms
    Distance vector routing
    Link state routing
    Flooding
  Routing protocols
    Routing Information Protocol (RIP)
    Open Shortest Path First (OSPF)
    Border Gateway Protocol (BGP)
Read Introduction and Sections 5.2.4-5.2.5
Read Sections 5.6.6 and 5.6.7
Notes: Video Module 5-02

## Slide 10: Routing Policy: Updating the Routing Tables
Manual
Using daemons on the routers (L3 switches):
  A daemon is a piece of software continuously running: it uses some algorithm to find paths and some protocols to communicate with other routers to gather information and send out information.

## Slide 11: Routing Policies (Algorithms) and Protocols
Routing policies (algorithms)
  Distance vector routing (DVR)
  Link state routing (LSR)
  flooding
Routing protocols
  Interior gateway protocols (IGP)
    Routing Information Protocol (RIP)
    Open Shortest Path First (OSPF)
  Exterior gateway protocol (EGP)
    BGP
Protocol | Policy/Algorithm
RIP | DVR
OSPF | LSR
BGP | Path Vector Protocol

## Slide 12: Distance Vector Routing
A node periodically
  tells to its neighbors only
  its distance to EVERY NODE in the network
Example:
  Initially (each node knows only about cost to its neighbors only):
    A  vector = (0,1,4,inf),
    B  vector = (1,0,1,1)
    C  vector = (4,1,0,3)
    D  vector = (inf,1,3,0)
  In Round 1, each node sends its vector
  After one round, every node will know the shortest path and the gateway
A
B
D
C
1
1
1
4
3
 | A | B | C | D
A | 0 | 1(B) | 2(B) | 2(B)
B | 1(A) | 0 | 1(C) | 1(D)
C | 2(B) | 1(B) | 0 | 2(B)
D | 2(B) | 1(B) | 2(B) | 0
Routing Table (Gateways)

## Slide 13: Distance Vector Routing (Problems!!!)
When ?
  Links go down
What kind of problem ?
  Count-to-infinity
  Example
    Initially
    A (0,1,inf)
    B (1,0,1)
    C (inf,1,0)
Solution
  path vector
    Send the distance vector but with the path also
A
B
C
1
1
X
(0,1,inf)
(1,0,1)
(0,1,2)
(0,1,2)
(1,0,3)
(0,1, 4)
(1,0, 5)
(0,1, 6)
(1,0, 7)
X
(1,0,1)

## Slide 14
Link-State Routing
A node
  tells EVERY node (through flooding)
  its distance to its immediate NEIGHBORS
How ?
  Send link-state packets (LSP)
  Using controlled flooding
  Use Dijkstra’s algorithm or Bellman-Ford
A
B
D
C
1
1
1
4
4

## Slide 15: Internal and External Protocols
LANs
Internet Backbone
Autonomous
Systems
Autonomous
Systems
Autonomous
Systems
Autonomous
Systems
Exterior Gateway
Protocol
Interior Gateway
Protocol

## Slide 16: Routing Policy Protocols
How to update the routing tables?
  Routing algorithms
    Distance vector routing
    Link state routing
  Routing protocols
    Interior
      Routing Information Protocol (RIP)
      Open Shortest Path First (OSPF)
    Exterior
      Border Gateway Protocol (BGP)
Read Introduction and Sections 5.2.4-5.2.5
Read Sections 5.6.6 and 5.6.7
Notes: Video Module 5-03

## Slide 17: RIP (RFC 1058) (Routing Information Protocol)
Interior gateway protocol
Distance vector algorithm
Uses split horizon to avoid count-to-infinity (Does not advertise a cost to a neighbor if it is a next hop for that destination)
Exchange each 30s
Time-out after 180 s.

## Slide 18: OSPF (RFC 1247) (Open Shortest Path First)
Interior gateway protocol
Link state protocol
Uses directly IP (while RIP uses UDP)

## Slide 19: BGP (RFC 1267) (Border Gateway Protocol)
Exterior gateway protocol
(Exception: BGP uses TCP !!!!)
Path Vector protocol (+ policy attributes)
Topology may be loop-free (BGP guarantees loop-freeness)

## Slide 20: A Mechanism (IP)
What is a routing mechanism?
The Internet Protocol (IP) is a mechanism
  How is an IP packet carried?
  The IP header
  IP Addresses
  IP subnetting
Read Section 5.6 up to 5.6.1
Notes: Video Module 5-04

## Slide 21: Routing Mechanism
Takes the decision how to route
Examples:
  Early Exit (known also as Hot Potato)
  IP (Internet Protocol)
These mechanisms do NOT modify the routing tables. They may read them.
For example, the IP protocol implements on each Internet host a mechanism to route. We will study what it does to route

## Slide 22: A Connectionless Network Layer: the Internet Protocol (IP)
The Internet Protocol is implemented on every:
  host that is connected to Internet
  router on a LAN connected to the Internet
  router on the backbone
  L3 switch on Internet
Application
Transport
Network IP
Link Layer

## Slide 23: Fundamental Idea of IP
Routes between networks.
Why? It makes routing tables shorter

## Slide 24
IP Packet
An IP packet is encapsulated in a frame ([Data] Link Layer)
Payload
Dest
Source
Type
6
6
2
46-1500
CRC
Preamble
IP Packet
0x0800
Header

## Slide 25
IP Header
31
0
15 16
V
IHL
TOS
Total Length
16-bit identification
Flgs
13-bit frag. offset
TtL
Protocol
Header Checksum
32-bit source IP address
32-bit destination IP address
Options (Variable 0 ---> ??)
Data Payload (TCP segment,
or UDP Datagram, or ICMP ….)

## Slide 26: IP Header Fields (1/2)
V : 4-bit number indicating the version
HL: 4-bit number indication the number of 32-bit words making the header. This number hints to whether the header contains options fields or not. If HL = 5, the header does not include any options.
TOS: Type Of Service. Indicates to the router the type of service this packet prefers. Specifically, it indicates the quality metrics to optimize: throughput, delay, cost….
Total Length: total number of bytes making the packet.
Identification: this 16-bit number identifies a packet (a fragment)
Flags: 3 bits (two of them (DF and MR) related to fragmentation and one unused)
Fragment Offset: 13 bit number indication the fragment number in a packet

## Slide 27: IP Header Fields (2/2)
TTL: Time To Live. This 8-bit field determines the maximum number of hops the packet should travel. TTL is decremented at each router. If TTL reaches 0, the router drops the packet.
Protocol: this 8-bit number indicates the “type” of payload (=6 for TCP, =17 for UDP, and =1 for ICMP
Checksum: this 16-bit number is the checksum on the HEADER. The header is organized as 16 bit words. All the words are added such that whenever there is a carry C, that carry C is simply added to the running sum. When the sum S is computed, the checksum is set to ~S (NOT(S), i.e, one-complement of S).
Source: 32 bit bit Source address.
Destination: 32 bit bit Destination address.
Options: cover special features.

## Slide 28: IP Addresses
What is a routing mechanism?
The Internet Protocol (IP) is a mechanism
  How is an IP packet carried?
  The IP header
  IP Addresses
  IP subnetting
Read Section 5.6.2
Notes: Video Module 5-05

## Slide 29: IP Address (Review)
IPv4
32 bits
8 bits
8 bits
8 bits
8 bits

## Slide 30
IP(v4) Address Structure (1/2)
Recall: IP routes between networks
An IP address will have two pieces of information:
  A Network ID (netid)
  A Host ID (hostid)
What should be the value of n?
netid
n bits
hostid
32-n bits
IP Address
32 bits

## Slide 31
IPv4 Address Structure (2/2): What Should be the value of n?
How to choose n?
Let us try different different values on and see how many networks and hosts per network we can have.
netid
n bits
hostid
32-n bits
IP Address
32 bits
N | Number of Networks | Number of Hosts / Network
2 | (4) | (~1 billion)
8 |  | 
16 | (65,536) | 
24 |  | 
N | Number of Networks | Number of Hosts / Network
2 |  | 
8 |  | 
16 |  | 
24 |  | 

## Slide 32
IPv4 Address Structure (2/2): What Should be the value of n?
How to choose n?
Let us try different different values on and see how many networks and hosts per network we can have.
netid
n bits
hostid
32-n bits
IP Address
32 bits
N | Number of Networks | Number of Hosts / Network
2 | (4) | (~1 billion)
8 |  | 
16 | (65,536) | 
24 |  | 
N | Number of Networks | Number of Hosts / Network
2 |  | 
8 |  | 
16 |  | 
24 |  | 

## Slide 33
Internet Addresses : A Compromise … Classes
Having different classes of addresses
  Class A
  Class B
  Class C
  Class D
  Class E
0
netid
hostid
7bits
24 bits
1
netid
hostid
14 bits
16 bits
0
1
netid
hostid
21 bits
8 bits
1
0
1
Multicast group ID
28 bits
1
1
0
1
Future use
27 bits
1
1
1
0

## Slide 34
Addresses Range By Classes
Ranges for the dotted decimal notation: W.X.Y.Z
  Class A : 0 - 127*
  Class B : 128 - 191
  Class C : 192 - 223
  Class D : 224 - 239
  Class E : 240 - 254

## Slide 35
Special/Reserved Internet Addresses
This host
Local host
Local broadcast
Remote broadcast
Loopback 127.X.X.X
Network Address Translation:
  Can be used internally (not on Internet)
    10.0.0.0 - 10.255.255.255 (: ~16 millions hosts)
    172.16.0.0. - 172.31.255.255 (: ~1 million hosts)
    192.168.0.0 – 192.168.255.255 ( : ~ 64K)
000000000000…..000000000000000000
32 bits
00000….0000000
hostid
1111111111111…..11111111111111111
11111111111…..111111111
NetID

## Slide 36
Internet Addresses (Cont’d)
Unicast addresses (Classes A, B, and C)
Multicast addresses (Class D)

## Slide 37: Subnets
What is a subnet?
Why subnetting?
How is subnetting done?
  A key tool: the subnet mask
Read Section 5.6.2
Notes: Video Module 5-06

## Slide 38
Subnetting
What is a subnet?
  It is a network that is part of another larger network (the subnet uses a subset of the addressing space of the network).
  Example:
    Auburn is assigned the network with netid 131.204.0.0
    The Auburn network is a class B network
Why subnetting ?
  A class A (or even Class B) network has a large number of hosts (16M for Class A and 65,534 for a Class B)
  In general, hosts on the same network will share a broadcast medium. 65,534 hosts are too many to share a medium.
How is it done ?
  Notion of subnet mask

## Slide 39
Subnetting (RFC 950)
1
netid
hostid
14 bits
16 bits
0
Class B
netid hostid
m bits 32-16-m bits
Example : Subnet AU network
131.204.0.0
netid hostid
5 bits
We divide the 16 bits addressing space
11 bits
Problem : How to know the number m of bits of the subnet ID?
In our example, the subnet ID has 16 bits + 5 bits = 21 bits…..
Answer:
  use a subnet mask that is a binary number starting with 21 ones and finishing with 11 zeros
Here the subnet mask = 1111 1111 1111 1111 1111 1000 0000 0000
Subnet ID = IP Address & subnet Mask (Bitwise AND)

## Slide 40
Subnet Mask
Example 1:
- What is the subnet ID of IP address 131.204.65.34 if the subnet mask is 255.255.255.0?
- 131.204.65.34 = 1000 0011 1100 1100 0100 0001 0010 0010
- 255.255.255.0 = 1111 1111 1111 1111 1111 1111 0000 0000
- Subnet ID = Bitwise IP&Mask
Bitwise IP&Mask = 1000 0011 1100 1100 0100 0001 0000 0000 = 131.204.65.0
- Subnet ID = 131.204.65.0
Example 2:
- What is the subnet ID of IP address 131.204.65.34 if the subnet mask is 255.255.255.240?
- 131.204.65.34 = 1000 0011 1100 1100 0100 0001 0010 0010
- 255.255.255.240 = 1111 1111 1111 1111 1111 1111 1111 0000
- Subnet ID = Bitwise IP&Mask
Bitwise IP&Mask = 1000 0011 1100 1100 0100 0001 0010 0000 = 131.204.65.32
Example 3:
- What is the subnet ID of IP address 131.204.65.34 if the subnet mask is 255.255.240.0?
- 131.204.65.34 = 1000 0011 1100 1100 0100 0001 0010 0010
- 255.255.240.0 = 1111 1111 1111 1111 1111 0000 0000 0000
- Subnet ID = Bitwise IP&Mask
Bitwise IP&Mask = 1000 0011 1100 1100 0100 0000 0000 0000 = 131.204.64.0

## Slide 41
Checking Whether Two IP Addresses Are on the Same Subnet
Idea : IP1 IP2
& (Bitwise AND)
Subnetmask
Subnetmask
= SubnetID1
If subnet IDs equal then IP1 and IP2 are on the same subnet
How to know that two hosts with IP addresses IP1 and IP2, respectively
are one the same subnet?
= SubnetID2
&

## Slide 42: Shorthand Subnet Mask Notation (/m)
Shorthand notation for subnet mask:
  How to express an IP 131.204.65.34 with a subnet mask is 255.255.255.0?
  Shorthand is 131.204.65.34/24
  Why 24?
  Subnet mask = 255.255.255.0 = 1111 1111 1111 1111 1111 1111 0000 0000
  There are 24 ones in the subnet mask.
Example 1: How to express an IP 131.204.65.34 with a subnet mask is 255.255.255.240?
  Subnet mask = 255.255.255.240 = 1111 1111 1111 1111 1111 1111 1111 0000
  Shorthand is 131.204.65.34/28
Example 2: How to express an IP 131.204.65.34 with a subnet mask is 255.255..240.0?
  Subnet mask = 255.255.240.0 = 11 1111 1111 1111 1111 0000 0000 0000
  Shorthand is 131.204.65.34/20

## Slide 43: Devices Connecting Machines
If two machines M1 and M2 have IP addresses with different subnet IDs, there is necessarily a router (or an L3 switch) on the path between M1 to M2.
The network interfaces of a router (L3 switch) have addresses that have different subnet IDs.

## Slide 44: IP Routing
How to select the next router (hop)?
  Routing table
  How does IP use the routing table?
Read Section 5.6.2
Notes: Video Module 5-07

## Slide 45
IP Mechanism
Consider a machine M with IP address IPm that is handed an IP packet P with a destination IP address IPd. IP on Machine M will handle P as follows:
  if (IPd = IPm) { // is the packet P for ”me” (Machine M)
    hand Packet P to appropriate transport layer protocol (based on protocol #)
  } else {
    if (IPd local to one of my interfaces) { // Is M on the same network as IPd? (Local)
      Get the MAC Address MACd of the interface having IP address IPd (See ARP)
      Ask data link layer to send Packet P to Machine with MAC address MACd.
    } else { // M is on a different network than IPd
      Read Routing Table to find a router R to forward Packet P
      Get MAC Address MACR of the router
      Ask data link layer to send Packet P to Machine with MAC address MACR.
      }

## Slide 46
IP Mechanism Example 1 (Illustration)
Suppose that the transport layer (TCP or UDP) on Host 1 hands to IP an IP packet to send to Host 2. IP1 = 192.32.65.7/24 and IP2 = 192.32.65.5/24.
Subnet ID for IP1 = 192.32.65.7 & 255.255.255.0 = 192.32.65.0
Subnet ID for IP2 = 192.32.65.5 & 255.255.255.0 = 192.32.65.0
The subnet IDs are equal: Destination IP2 is local
Host 1 will then get the MAC address of Host 2 (i.e., E2), put the packet P in a frame, send this frame to MAC address E2.

## Slide 47
IP Mechanism Example 2 (Illustration)
Suppose that the transport layer (TCP or UDP) on Host 1 hands to IP an IP packet to send to Host 3. IP1 = 192.32.65.7/24 and IP3 = 192.32.63.3/24.
Subnet ID for IP1 = 192.32.65.7 & 255.255.255.0 = 192.32.65.0
Subnet ID for IP3 = 192.32.63.3 & 255.255.255.0 = 192.32.63.0
The subnet IDs are different: Destination is on a different network
Host 1 will read the routing table and find that the router has MAC address E3.
Host 1 will then get the MAC address of Router (i.e., E3), put the packet P in a frame, send this frame to MAC address E3.

## Slide 48
IP Routing : The Routing Table
Based on a routing table with entries having
  Destination IP addr (host ID or net ID)
  Subnet Mask
  Next hop router IP address
  flags (hostid or netid, next hop or connected interface…)
  network interface
Destination IP | Subnet Mask | Router IP Address | Network Interface Card
131.204.0.0 | 255.255.0.0 | 134.89.200.54 | ………
0.0.0.0 |  | 200.134.67.24 | …….

## Slide 49
IP Routing : Selecting the next Hop (Router)
1) Try to find a complete IP address match in the routing table
2) If 1) fails, then try to find the longest match with some network id. If the subnet ID of the destination matches with 131.204.0.0 and 131.204.65.0 then choose 131.204.65.0 in the routing table
if 1) and 2) fail search for default router (entry 0.0.0.0)

## Slide 50: IP “Helpers”
ARP (Address Resolution Protocol) : RFC 826
DHCP (Dynamic Host Configuration Protocol) (RFC 1541)
ICMP (Internet Control Message Protocol) (RFC 792)
Read Section 5.6.4
Notes: Video Module 5-08

## Slide 51: ARP (Address Resolution Protocol) What?
ARP (Address Resolution Protocol) : RFC 826
  Maps an IP address to a MAC address
  Input: IP address IPa
  Output: MAC address of interface having IP address IPa.
Transport Layer
Network Layer
Link Layer
Physical Layer
IP
ARP
What is Mac Address for IPa? 
 Here is Mac Address for IPa

## Slide 52: ARP (Address Resolution Protocol) How?
When ARP receives a request (“What is the MAC Address for IP Address IPa?)
  ARP searches in its cache for an entry with IPa
  If there is an entry, it takes the associated MAC address and sends it back to IP.
  If it does NOT find an entry, it performs these actions:
    It broadcasts on the local network the message “Who has the IP address IPa?”
    It waits for a response…
    When it receives a response with the associated MAC address, it stores it in its cache and sends the MAC address to IP.

## Slide 53: DHCP (Dynamic Host Configuration Protocol)
Every machine needs the following information to communicate over the Internet
  IP address
  Subnet mask
  IP address of the DNS server (DNS maps host names to IP addresses)
  IP address of the default gateway (Router to go to the Internet)
How to configure the machine with this information?
  Manually?
  Use a configuration file?
  Use DHCP
    Each machine should have a “reachable” DHCP server on the network
    The DHCP client on the machine will (at startup in general):
      discover the DHCP server
      collect the IP address, subnet mask, IP address of DNS server, and the IP address of default gateway

## Slide 54: ICMP (Internet Control Message Protocol)
This protocol helps when anomalies occur
  TTL reaches 0 and the packet must be dropped
  Routing error
  An IP packet must be fragmented, but its fragmentation flag does not allow it…
When an anomaly occurs, ICMP
  builds an ICMP message that contains the beginning of the “faulty” packet (first 64 bytes including the IP header and the transport layer header)
  Sens back a message to the source of the “faulty” packet.

## Slide 55: Wrap-Up
Get familiar with the Network Layer
Learn and understand Routing Policies (algorithms and protocols)
Learn how to Update Routing Tables (Routing policy)
Learn about the routing mechanism (IP) for Routing over the Internet
Learn about some IP helpers (IP)
Notes: Video Module 5-09