## Slide 1: Transport Layer
Notes: Video Module 6-01

## Slide 2
Overview
Objectives
Learn and understand the transport layer (in general).
Learn and understand the Transmission Control Protocol (TCP).
Learn and understand the User Datagram Protocol (UDP).
Requirements
Read Sections 6.1.1-6.1.2, 6.2.1, 6.2.4, and 6.2.5.
Read Section 6.5 (pp552-581).
Read Section 6.4 (pp 541-543. Stop at RPC (excluded)).

## Slide 3: Introduction
Transport layer in the OSI reference model
Services of the transport layer
  Addressing,
  Reliability
  Flow control
  Congestion control
Read Sections 6.1.1-6.1.2, 6.2.1, 6.2.4, and 6.2.5.

## Slide 4: What is the Transport Layer ?
It provides a service (to define) to the session layer (in OSI)
It request service from the network layer
Session
Transport
Network
Link Layer

## Slide 5: Why Do We need a Transport Layer ?
Because the network layer may be an unreliable (lousy) agent:
  It may loose packets
  It may reorder packets
  It may duplicate packets
The network layer identifies HOSTS (interfaces more precisely) only!!!
Moreover, in general a connectionless network layer does not provide any flow or congestion control.

## Slide 6: Transport layer Provides END-TO-END Services
Reliability
Addressing
Flow control
Congestion control
  In addition, it may offer some Quality of Service (QoS) guarantees

## Slide 7: END-TO-END !!!
Upper layers
Transport
Network
Link Layer
Upper layers
Transport
Network
Link Layer
Network
Link Layer
Network
Link Layer
Network
Link Layer
Network
Link Layer
IEEE 802.3
ATM
Satellite link
Phone line

## Slide 8: Reliability
How to provide reliability ?
In general, reliability is done by:
  Error Detection + Retransmission because of corrupting channel
  Must number units of communications (TPDU, segments) if acks can be corrupted
  Timeout at sender + Retransmissions because of lossy channel

## Slide 9: A form of Addressing
An entity for the network layer may have multiple “connections”, how to differentiate them ?
The transport layer assigns different “numbers” to different connections on the same host

## Slide 10: Flow Control
A fast sender should now overflow a slow RECEIVER.. How to avoid this ?
The receiver advertizes the size of its input buffers.
The sender limits the number of outstanding data units to the size advertized.

## Slide 11: Congestion Control
A sender should not overflow the intermediary devices on the NETWORK. How ?
  Use losses as indication of congestion (when devices overflow, they drop packets)
  Use of variations if round trip time (when queues get longer, delay spent in devices increase)
Congestion control is a difficult problem still intensely studied by researchers.

## Slide 12: Transport Protocols on The Internet
TCP: (Transmission Control Protocol RFC 793) offers a reliable connection-oriented in order byte stream
UDP : (User Datagram Protocol RFC 768) offers an unreliable connectionless byte stream.

## Slide 13: Transmission Control Protocol (TCP RFC 793)
TCP in the TCP/IP Reference Model
Services provided by TCP
  Addressing,`
    TCP Header
    Header fields related to addressing
  Reliability
  Flow control
  Congestion control
Read Sections 6.2.1 and 6.5.4,
Notes: Video Module 6-02

## Slide 14: Where in TCP/IP Model ?
Application
Transport TCP
Network
Link Layer

## Slide 15: Addressing in TCP
TCP uses Ports
A port identifies a TCP (server or client).
At the application level, the TCP (server or client) is bound to a port number
The port number is a 16 bit number (0-65535)
How does a TCP server and client exchange port numbers?
Answer:
  The port numbers are carried inside the TCP header
Where is the TCP header?

## Slide 16: Where is a TCP Segment in a Frame? (Encapsulation)
A frame (Link Layer) encapsulates a packet (Network Layer)
A packet (Network Layer) encapsulates a segment (Transport Layer)
The segment (Transport Layer) encapsulated a message (Application Layer)

## Slide 17
Relation to IP Header
31
0
15 16
V
HL
TOS
Total Length
16-bit identification
Flgs
13-bit frag. offset
TTL
Protocol
16-bit Hdr Checksum
32-bit source IP address
32-bit destination IP address
Options (Variable 0 ---> ??)
Data (TCP segment, or UDP Dtg,
or ICMP ….)
IP
Header

## Slide 18: TCP Header
16-bit src port number
16-bit dst port number
32-bit sequence number
32-bit acknowledgement number
4-bit HL
Flags
16-bit window size
16-bit checksum
16-bit urgent pointer
Options
Data (Application Message)
16-bit Source port #
16-bit Destination port #

## Slide 19: Transmission Control Protocol (TCP RFC 793)
TCP in the TCP/IP Reference Model
Services provided by TCP
  Addressing,`
    TCP Header
    Header fields related to addressing
  Reliability
    Problem: IP offers just a best-effort service
    Three phases for a connection
      Opening,
      data exchange,
      closing
    Sequence numbers
    Recovering Corrupted/Lost Segments
    Sliding windows
  Flow control
  Congestion control
Read Sections 6.5.4, 6.5.5, and 6.5.6
Notes: Video Module 6-03

## Slide 20: Service Offered by IP
Best effort service
  it may loose packets
  it may reorder packets
  it may duplicate packets

## Slide 21: Service Offered by TCP
A connection-oriented
Reliable
Byte stream
Application
TCP
Network (IP)
Link Layer
Reliable byte stream
Looses,
Reorders,
Duplicates packets

## Slide 22: Phases of a TCP Connection
Opening
Full duplex data exchange
Closing

## Slide 23: Function of Opening a Connection
Client informs server (creation of tcp control block)
Client and server exchange initial sequence numbers : (TCP numbers bytes)
Client and server “negotiate” maximum segment size (mss) and window size

## Slide 24: Opening a Connection: Three-Way Handshake
time
Client
Server
SYN 1200:1200
mss 1024
SYN 34901:34901
ack 1201 mss 1024
Ack 34902

## Slide 25: Closing a Connection
time
Client
Server
FIN
Ack of FIN
Ack of FIN
App. closes
EOF to app.
FIN
Data

## Slide 26: Data Exchange: Sequence Numbers
A TCP Header includes two 32-bit sequence numbers:
  A sequence number: it is the sequence number of the first byte in a segment
  An ack. number a: it is an acknowledgment number a that means:
    All bytes with sequence number up to a-1 were correctly received in order
    The next expected byte is the byte with sequence number a.
  Example 1:
    Suppose that a TCP client receives a segment containing 5 bytes such that the sequence number is 1000.
    The TCP client will respond with an acknowledgement number ……..
1000
1004
1005

## Slide 27: Sequence/Ack Numbers in the TCP Header
16-bit Source port number
16-bit Destination port number
32-bit sequence number
32-bit acknowledgement number
4-bit HL
Flags
16-bit window size
16-bit checksum
16-bit urgent pointer
Options
Data (Application Message)
32-bit sequence number
32-bit acknowledgement number
A TCP Header includes two 32-bit sequence numbers:
  A 32-bit sequence number: it is the sequence number of the first byte in a segment
  A 32-bit ack. number a: it is an acknowledgment number a that means:
    All bytes with sequence number up to a-1 were correctly received in order
    The next expected byte is the byte with sequence number a.

## Slide 28: Transmission Control Protocol (TCP RFC 793)
TCP in the TCP/IP Reference Model
Services provided by TCP
  Addressing,`
    TCP Header
    Header fields related to addressing
  Reliability
    Problem: IP offers just a best-effort service
    Three phases for a connection
      Opening,
      data exchange,
      closing
    Sequence numbers
    Recovering Corrupted/Lost Segments
    Sliding windows
  Flow control
  Congestion control
Read Section 3.1.4 (from data link layer… but think end to end)
Notes: Video Module 6-04

## Slide 29: Data Exchange
Data Exchange is bidirectional (both endpoints can send)
TCP must handle 3 functions :
  Error detection and recovery
  Flow control
  Congestion control
TCP must adapt to :
  kind of traffic (Bulk or interactive)
  Network conditions

## Slide 30: Service Offered by IP
Best effort service
  it may loose packets
  it may reorder packets
  it may duplicate packets

## Slide 31: What Can Happen to A Segment?
A segment can:
  reach its destination unaltered
  reach destination corrupted
  reach the destination out of order
  get lost before reaching the destination
  get duplicated

## Slide 32: How to Deal with Corrupted Segments?
Two questions:
  How does TCP detect that a segment is corrupted?
  Answer:
    Use a checksum: it covers the TCP header and the payload (application message). Computed as shown in the module about the Data Link Layer. Compute the sum S of all 16-bit numbers (with carry wrap-around). Checksum = ~S.
  How does TCP recover a corrupted segment?
    TCP resends the segment.
16-bit Source port number
16-bit Destination port number
32-bit sequence number
32-bit acknowledgement number
4-bit HL
Flags
16-bit window size
16-bit checksum
16-bit urgent pointer
Options
16-bit checksum
Data (Application Message)

## Slide 33: How to Deal with Out-of-Order Segments?
Consider a TCP sender which sent 3 segments (1000, 1006, and 1010)
  The first segment with sequence number 1000 is received unaltered
  The TCP receiver will acknowledged it with an acknowledgement number = 1006 (next expected byte)
  The second segment gets lost
  The receiver is unaware that the segment (1006) is lost
  The third segment with sequence number 1010 is received unaltered.
  Now, the receiver knows that something happened to the segment with sequence # 1006:
    Segment (1006) is out-of-order or is lost.
    The TCP receiver sends another acknowledgment identical to the previous: it is called a duplicate acknowledgement.
If the sender receives three duplicate (dupacks), it assumes the segment is lost.
TCP
Sender
1000
1006
1010
TCP
Receiver
Ack = 1006
X
Lost
Ack = 1006
Dupack

## Slide 34: How to Deal with Lost Segments?
Consider a TCP sender which sent 2 segments (1000 and 1006) and does not send any other segment for some time
  The first segment with sequence number 1000 is received unaltered
  The TCP receiver will acknowledged it with an acknowledgement number = 1006 (next expected byte)
  The second segment gets lost
  The receiver is unaware that the segment (1006) is lost
  No other segment is sent by the TCP sender.
  How can the TCP sender or TCP receiver realize that Segment (1006) is lost?
  Answer:
    The TCP sender sets up a timer before sending a segment: if the TCP sender does not receive an ack for that segment within some time, it will timeout and resend the segment.
    A timeout mechanism at the sender is the only solution.
TCP
Sender
1000
1006
TCP
Receiver
Ack = 1006
X
Lost

## Slide 35: Notion Of Sliding Window
What is the problem with stop-and-wait protocol ?
  Assume a network path with a bottleneck link being a 20 Mbps and propagation time of 50ms, what is the highest throughput that we can achieve with a 1250 bytes segment?
Solution : a window-based protocol
  Keep sending new segments without waiting for acknowledgements.

## Slide 36: Sliding Window (Maintained by the Sender)
Sequence
number
Sent and
acked
34 35 36 37 38 39 40 41 42 43 44 45 46…...
Sent, not
acked
May be sent
if data available
Cannot be
sent
Offered Window Wnd
(advertised by receiver or limited by network conditions)

## Slide 37: Sliding Window (Maintained by the Sender)
Sequence
number
Sent and
acked
34 35 36 37 38 39 40 41 42 43 44 45 46…...
Sent, not
acked
May be sent
if data available
Cannot be
sent
Offered Window Wnd
(advertised by receiver or limited by network conditions)

## Slide 38: Transmission Control Protocol (TCP RFC 793)
TCP in the TCP/IP Reference Model
Services provided by TCP
  Addressing,`
    TCP Header
    Header fields related to addressing
  Reliability
    Problem: IP offers just a best-effort service
    Three phases for a connection
      Opening,
      data exchange,
      closing
    Sequence numbers
    Recovering Corrupted/Lost Segments
    Sliding windows
  Flow control
  Congestion control
Read Introduction to 6.4
Notes: Video Module 6-05

## Slide 39: Flow Control /Congestion Control
Flow Control
  Flow control is a strategy to insure that a fast sender does not overrun a slow receiver. A slow receiver is a receiver that processes incoming packets at a slower rate than the sending rate. If the receiver is overwhelmed, its input queue will fill up and packets will get dropped.
Congestion Control
  Congestion control is a strategy to avoid that intermediary nodes are overrun. An intermediary node will get overrun if the incoming traffic rate is larger than the outgoing traffic rate.

## Slide 40: Flow Control /Congestion Control in TCP
TCP achieves Flow Control and Congestion Control by adjusting the Offered Window Wnd
  Flow control is achieved by the receiver which limits the sender’s offered window by advertising a window Wa side (it is the maximum size of the incoming buffer). The receiver tells (advertises to) the sender the maximum size of its offered window.
  Congestion control is achieved by the sender which will try the guess the maximum size of the offered window to avoid overrunning the intermediary nodes. This maximum size of the offered window is a variable (at the sender) called cwnd : the size of the congestion window. cwnd is a variable maintained by the sender.
TCP set Wnd to min(Wa, cwnd)
Why not set Wnd to the smallest possible value?
  Answer : the throughput and efficiency will be terribly low (recall stop-and-wait)
Sequence #
Sent and
acked
34 35 36 37 38 39 40 41 42 43 44 45 46…...
Sent, not
acked
May be sent
if data available
Cannot be
sent
Offered Window Wnd
(advertised by receiver or limited by network conditions)

## Slide 41: Flow Control in TCP
The receiver monitors its available input buffer size
When acknowledging segments, the receiver advertises (for the sender) its available input buffer size.
16-bit Source port number
16-bit Destination port number
32-bit sequence number
32-bit acknowledgement number
4-bit HL
Flags
16-bit window size
16-bit checksum
16-bit urgent pointer
Options
16-bit window size
Data (Application Message)

## Slide 42: Transmission Control Protocol (TCP RFC 793)
TCP in the TCP/IP Reference Model
Services provided by TCP
  Addressing,`
    TCP Header
    Header fields related to addressing
  Reliability
    Problem: IP offers just a best-effort service
    Three phases for a connection
      Opening,
      data exchange,
      closing
    Sequence numbers
    Recovering Corrupted/Lost Segments
    Sliding windows
  Flow control
  Congestion control (Part I)
Read Sections 6.5.10
Notes: Video Module 6-06

## Slide 43: END-TO-END makes Congestion Control Hard!
Upper layers
Transport
Network
Link Layer
Upper layers
Transport
Network
Link Layer
Network
Link Layer
Network
Link Layer
Network
Link Layer
Network
Link Layer
IEEE 802.3
ATM
Satellite link
Phone line

## Slide 44: How Is the Window Size Wnd Set ?
Flow control : Receiver advertises the window size Wa. Sender can send at most Wa bytes without receiving acknowledgements.
Congestion control : TCP will adapt to “network conditions” and set a limit cwnd. This maximum size of the offered window is a variable (at the sender) called cwnd : the size of the congestion window. cwnd is a variable maintained by the sender.
The offered window size Wnd is set to min(Wa, cwnd)

## Slide 45: Congestion Control: How Is cwnd Maintained?
Objective:
  The objective is to maximize the throughput (efficiency).
  Maximizing throughput calls to increase the window size Wnd, and therefore cwnd.
  But, increasing cwnd increases the risk of overflowing the input buffer on some intermediary device.
  In addition, the objective is fairness: users should achieve similar throughputs.
  Question: How to achieve the highest and fair throughput without overflowing intermediary devices?
This problem is similar to the Weekly Pocket Money Demand: (How can a child get the most pocket money possible?)
Suppose that:
  Parents set a fixed total weekly allowance B for ALL children
  The allowance B is not known by the children
  Each child does not know what, when, or whether siblings asked for or got each week.
  Not all children ask for money each week.
  If the child asks for an amount cwnd less than what parents still have, the parents grant it even if it is the total allowance B.
  Now, if the child asks for more than the remaining available B, the parents SMACK the child and confiscate all money the child has.
  What should be the strategy of the child to get the highest amount of pocket money and avoid getting smacked too often?

## Slide 46: Strategy for the Weekly Pocket Money Demand Problem
Strategy:
  Let cwnd be the amount of money to ask.
  Initially set cwnd to 1 (cwnd = 1)
  If I was successful last week (no smacking!), double cwnd (cwnd = 2*cwnd)
  If I got smacked:
    Remember the threshold amount cwnd for which I got smacked. The idea is to become less greedy when I reach half that threshold (I want to avoid smacking). So threshold = cwnd / 2; (1/2 is a security coefficient)
  Now that I learned the threshold, I will change my strategy to ask money when I was successful last week. FOR EACH successfully granted dollar, I will do this:
    .
      // greedy, pushy
    else
      . // careful, smacking avoidance
This strategy is proven to be stable and fair
  Stable: the parent will never go bankrupt (though may go to prison for child abuse*)
  Fair : over time each child in the family will get a fair amount of pocket money.
TCP uses this strategy.
Let us revisit the congestion problem in light of the Weekly Pocket Money Demand.

## Slide 47: Transmission Control Protocol (TCP RFC 793)
TCP in the TCP/IP Reference Model
Services provided by TCP
  Addressing,`
    TCP Header
    Header fields related to addressing
  Reliability
    Problem: IP offers just a best-effort service
    Three phases for a connection
      Opening,
      data exchange,
      closing
    Sequence numbers
    Recovering Corrupted/Lost Segments
    Sliding windows
  Flow control
  Congestion control (Part II)
Read Sections 6.5.10
Notes: Video Module 6-07

## Slide 48: Congestion Control: How Is cwnd Maintained?
Objective:
  The objective is to maximize the throughput (efficiency).
  Maximizing throughput requires to increase the window size Wnd, and therefore cwnd.
  But, increasing cwnd increases the risk of overflowing the input buffer on some intermediary device.
  In addition, the objective is fairness: users should achieve similar throughputs.
  How to achieve getting the highest and fair throughput without overflowing intermediary devices?
Let us revisit the congestion problem.
Suppose that:
  A bottleneck router/device has a fixed total available bandwith B.
  The available bandwith B is not known by the users using the same bottleneck router/device
  Each user does not know what, when, or whether the other users ask for or got each cycle.
  Not all users use the router/device each cycle.
  If the user asks for an amount less than what the router has, the router grants it all even if it is the total available B.
  Now, if the user sends more packets than what the router can handle (input buffer full), the router drops the packet(s).
  What should be the strategy of a user to get the highest bandwidth (throughput) and avoid packets drops?

## Slide 49: Strategy for the Congestion Control
Strategy: (Van Jacobson and Raj Jain)
  Let cwnd be the size of the congestion window.
  Initially set cwnd to 1 (cwnd = 1)
  If I was successful last transmission (acknowledgement), increment cwnd (cwnd = cwnd + 1)
  If I packet dropped:
    Remember the threshold amount cwnd for which I got the packet dropped. The idea is to become less greedy when I reach half that threshold (I want to avoid packet drops). So threshold = cwnd / 2; (1/2 is a security coefficient)
  Now that I learned the threshold, I will change my strategy to set my congestion windos when I get an acknowledgement (successful transmission). FOR EACH acknowledged segment, here is what I will do:
    .
      // slow start
    else
      // congestion avoidance (additive increase)
This strategy is proven to be stable and fair
  Stable: the network will not collapse
  Fair : over time each user will get a fair bandwith (throughput)
TCP uses this strategy.

## Slide 50: What If a Packet is lost ?
Two cases:
  If a timeout occurs (this means all packets in the outstanding window were lost), then
  If the sender receives three dupacks (duplicate acknowledgements)
    // Multiplicative Decrease

## Slide 51: TCP Reno Congestion Window With Timeout
Two cases:
  If a timeout occurs (this means all packet in the window were lost), then
  If the sender receives three dupacks (duplicate acknowledgements)
timeout
cwnd

## Slide 52: TCP Reno Congestion Window With Packet Loss
Two cases:
  If a timeout occurs (this means all packet in the window were lost), then
  If the sender receives three dupacks (duplicate acknowledgements) (isolated packet loss)
cwnd

## Slide 53: Congestion Control and the TCP Header
16-bit Source port number
16-bit Destination port number
32-bit sequence number
32-bit acknowledgement number
4-bit HL
Flags
16-bit window size
16-bit checksum
16-bit urgent pointer
Options
Data (Application Message)
32-bit sequence number
32-bit acknowledgement number
A TCP sender keeps track of the last sequence number sent and the highest acknowledgement received so far:
  A 32-bit sequence number: it is the sequence number of the first byte in a segment
  A 32-bit ack. number a: it is an acknowledgment number a that means:
    All bytes with sequence number up to a-1 were correctly received in order
    The next expected byte is the byte with sequence number a.

## Slide 54: User Datagram Protocol (UDP RFC 768)
UDP in the TCP/IP Reference Model
Relation to IP
Services provided by UDP
  Addressing
    UDP Header
    Header fields related to addressing
  Reliability
    Just detection
    Header fields related to error detection
Read Introduction to 6.4, and Section 6.4.1
Notes: Video Module 6-08

## Slide 55
Where in TCP/IP Model ?
Application
Transport UDP
Network
Link Layer

## Slide 56
Relation to IP Header
31
0
15 16
V
HL
TOS
Total Length
16-bit identification
Flgs
13-bit frag. offset
TTL
Protocol
16-bit Hdr Checksum
32-bit source IP address
32-bit destination IP address
Options (Variable 0 ---> ??)
Data (TCP segment, or UDP Dtg,
or ICMP ….)
IP
Header

## Slide 57: UDP Functions/Services
Offers a SIMPLE user access to a Datagram Service (Raw socket is accessible only to super users (root access))
A checksum service to detect corrupted packets
No reliability (No retransmission, no timeout, no care about MTU...)

## Slide 58: UDP Header
Source Port number (2 bytes)
Destination Port number (2 bytes)
Datagram length in bytes (header + payload)
Checksum (2 bytes)

## Slide 59: Checksum Computation
Checksum concerns PSEUDO header + data
Pseudo header contains:
  from the IP header
    IP source
    IP destination
    Protocol number (17)
  From the UDP header
    Source port #
    Destination port #
    UDP length

## Slide 60: Wrap Up
Learn and understand the transport layer (in general).
  Addressing, reliability, flow control, congestion control, QoS
Learn and understand the Transmission Control Protocol (TCP).
  Addressing (Port Numbers)
  Reliability (sequence number, ack. Number, checksum)
  Flow control (advertised window)
  Congestion control (Slow-start and congestion avoidance strategies)
Learn and understand the User Datagram Protocol (UDP).
  Addressing (Port Numbers)
  Reliability (detection only, checksum)
Notes: Video Module 6-09