## Slide 1
Course Notes Set 7: Verification and Validation
Computer Science and Software Engineering
Auburn University

## Slide 2: You are here
Lesson: Verification and Validation
Strategic Objective: understand the role and purpose of V&V in quality assurance
Tactical Objectives:
  understand the rationale and importance of V&V
  understand the management role in V&V
  know the V&V inputs and outputs at various parts of the life cycle
  understand the four major V&V techniques
  know the purpose, inputs, and process of each technique

## Slide 3: You are here (con’t)
Introduction
QA
CM
V&V
T&E
Metrics
First principles
  rationale
  role
Organizational activities
V&V approaches
  Formal review
  Walkthrough
  Audit
  Inspection
Assessing effectiveness

## Slide 4: COMP 6710 emphasis
Controlled and documented change
Configuration Management (CM)
Conformance with standards
Software Quality Assurance (SQA)
Traceability and congruence with requirements
Verification & Validation (V&V)
Software code exercise and assessment
Test and Evaluation (T&E)
Product with integrity
Notes: with this as a backdrop, we can see that the act of “quality assurance” is a complicated one, especially for software. To help us organize in our minds the concept of “quality assurance” we need to take a divide-and-conquer approach and look at QA as process (SQA), product (SCM), production (V&V and T&E)

## Slide 5: First principles
Software Verification and Validation
  ... is the discipline of verifying that products of each software life cycle phase comply with previous life-cycle phase requirements and establish the proper basis for initiating the next life cycle phase, and of validating that the completed end product complies with established software and system requirements.
  objective:
    verification: “are we building the product right”
    validation: “are we building the right product”
Traceability and congruence with requirements
Verification & Validation (V&V)
Quality Product

## Slide 6: First principles (con’t)
V&V ...
  ... is a defense against error prone software development and maintenance process
  ... is a form of testing
  ... is a way of tracking a project
  ... is a vehicle for educating users/sellers/buyers on product
  ... attempts to overcome limitations on code testing
  ... impacts maintenance
  ... impacts morale
Notes: V&V ...
  is a defense against ...
    complexity of software development and maintenance processes
    error frequencies for software work products
    error distribution throughout development phases
    increasing costs for error removal throughout the life cycle
  form of testing
    objectives
    human-based vs machine-based
    attitudes and norms
  tracking product
    individual developer tracking
    management tracking
    customer tracking
  education
    project understanding
    technical skills
  morale
    positive & negative impact depending on how conducted
  maintenance
    better docs, standardization, readability
  limitation of testing
    exhaustive testing impossible
    intermediate software products largely untestable

## Slide 7: First principles
V&V benefits
  Reduction in errors in the first production runs of maintenance changes (85% -> 20%) [Freedman]
  Reduction in errors in the first production run of a one-line maintenance change (55% -> 2%) [Freedman]
  77% reduction in production crashes during first six months of operation of a system [Freedman]
  88% reduction in field trouble reports [Freedman]
  Reduction of errors in COBOL code (5.5 E/KLOC -> 1.0 E/KLOC) [Freedman]
  Increased productivity through early detection and removal of errors. [Boehm]
  Removal of 30% to 70% of logic and design errors [Myers]

## Slide 8: First principles
Products typically addressed by V&V
  requirements
  specifications
  designs
  implementation
  changes
V&V Objectives
  correctness
  consistency
  necessity
  sufficiency
Notes: products
  req: provide informal statement of user needs
  spec: provide refinement of user needs which must be satisfied by product
  design: describes how specifications will be satisfied
  implementations: deliverable product (normally, code)
  changes: product modification due to corrective, adaptive, perfective actions
objectives
  correctness: the extent to which the product is error free
  consistency: the extent to which the product is consistent with itself and other products
  necessity: the extent to which everything in the product is necessary
  sufficiency: the extent to which the product is complete

## Slide 9: Organization perspective
V&V goals
  V&V activities are planned
  adherence to V&V process is verified
  role and results of V&V function communicated to all
  non-compliance detected, action taken

## Slide 10: Organization perspective (con’t)
Requirements
Concept
Design
Implementation
Test
Installation & Checkout
Operation & Maintenance
Management of V&V
V&V inputs
V&V tasks
V&V outputs
Notes: Note that there are V&V activities for each of the lifecycle phases.
Can think of this as the V part of the ETVX

## Slide 11: Concept phase V&V
V&V tasks
  concept documentation evaluation
Inputs
  development schedules
  concept documentation (e.g., SON, feasibility study, etc.)
Outputs
  Concept phase task reporting
  Anomaly reports
Notes: concept doc eval
  evaluate doc to determine if proposed concept satisfied user needs
  identify major constraints of interfacing system
  assess criticality of features

## Slide 12: Requirements phase V&V
V&V tasks
  requirements traceability analysis
  requirements evaluation
  requirements interface analysis
  test plan generation
Inputs
  concept documentation
  SRS
  interface requirements documentation
  user documentation
Outputs
  requirements phase task reporting
  test plan (system, acceptance)
  anomaly reports
Notes: tasks
  software req traceability analysis: trace SRS requirement to system requirements in concept documentation. Analyze identified relationships for correctness, consistency, completeness, accuracy
  software req eval. Evaluate SRS requirements for correctness, consistency, completeness, accuracy, readability, and testability. Assess how well SRS satisfies software system objectives. Assess the criticality of requirements to identify key performance or critical areas of software.

## Slide 13: Design phase V&V
V&V tasks
  design traceability analysis
  design evaluation
  interface analysis
  test plan generation
  test design generation
Inputs
  standards
  SRS
  SDD
  interface requirements documentation
  interface design documentation
  user documentation
Outputs
  design phase task reporting
  test plan (component, integration)
  test design (component, integration, system, acceptance)
  anomaly reports

## Slide 14: Implementation phase V&V
V&V tasks
  code traceability analysis
  code evaluation
  interface analysis
  test case generation
  test procedure generation
  component test execution
Inputs
  standards
  SDD
  source code
  executable code
  interface design documentation
  user documentation
Outputs
  implementation phase task reporting
  test cases (component, integration, system, acceptance)
  test procedures (component, integration, system)
  anomaly reports

## Slide 15: Test phase V&V
V&V tasks
  test procedure generation
  integration test execution
  system test execution
  acceptance test execution
Inputs
  source code
  executable code
  user documentation
Outputs
  test phase task reporting
  test procedures (acceptance)
  anomaly reports
Notes: tasks
  software req traceability analysis: trace SRS requirement to system requirements in concept documentation. Analyze identified relationships for correctness, consistency, completeness, accuracy
  software req eval. Evaluate SRS requirements for correctness, consistency, completeness, accuracy, readability, and testability. Assess how well SRS satisfies software system objectives. Assess the criticality of requirements to identify key performance or critical areas of software.

## Slide 16: Installation/Checkout V&V
V&V tasks
  installation configuration audit
  V&V final report generation
Inputs
  installation package
Outputs
  installation and checkout phase task reporting
  anomaly reports
  V&V phase summary report
Notes: tasks
  software req traceability analysis: trace SRS requirement to system requirements in concept documentation. Analyze identified relationships for correctness, consistency, completeness, accuracy
  software req eval. Evaluate SRS requirements for correctness, consistency, completeness, accuracy, readability, and testability. Assess how well SRS satisfies software system objectives. Assess the criticality of requirements to identify key performance or critical areas of software.

## Slide 17: Op & Maint phase V&V
V&V tasks
  anomaly evaluation
  proposed change assessment
  phase task reiteration
Inputs
  development schedules
  concept documentation
  SRS
  interface requirements documentation
  SDD
  interface design documentation
  source code
  executable code
  user documentation
  software management plan
  proposed/approved changes
  anomaly reports
Outputs
  updated software management plan
  O&M task reporting
  required phase outputs reiterated
  anomaly reports
Notes: tasks
  software req traceability analysis: trace SRS requirement to system requirements in concept documentation. Analyze identified relationships for correctness, consistency, completeness, accuracy
  software req eval. Evaluate SRS requirements for correctness, consistency, completeness, accuracy, readability, and testability. Assess how well SRS satisfies software system objectives. Assess the criticality of requirements to identify key performance or critical areas of software.

## Slide 18: Management of V&V activities
V&V tasks
  software V&V plan generation
  management review
  review support
Inputs
  production schedules
  status reports
  inputs/outputs from other phases
Outputs
  SVVP and updates
  test reporting
  phase V&V summary reports
  anomaly reports

## Slide 19: V&V Techniques
V&V is a form of testing
  uses human intellectual power to detect flaws
  frequently categorized as “static testing” approach (since code is not necessarily exercised)
  most notable approach to V&V is a review process
Goals of V&V reviews
  enhancing product through cost-effective, timely detection of defects
  promoting personal growth and communication among software development professionals
  fostering teamwork professionalism, participatory decision-making, and high morale
  enhancing the effectiveness of testing by detecting errors prior to testing
  find errors, not fix them

## Slide 20: V&V Techniques (con’t)
V&V challenges
  how do you motivate reviewers?
    organization review culture needed
    incentivize review process
  behavior of small groups may influence review outcome
    recognize pros/cons of group deviants
    beware of group think
    minimize domination of group by single member
  minimizing stress
    foster review culture
    define extent of management/customer participation in advance
    promote reviews as defect detection not personnel evaluation
  review logistics are a must
    time, location, duration, number of participants, physical arrangement

## Slide 21: V&V Techniques (con’t)
Formality
  V&V entails broad spectrum of reviews spanning from informal to formal
  formality of reviews determined by interaction with groups outside project scope
  generally, the more formal reviews involve product evaluation that is meant for more than the immediate use of the software author
  uses:
    to determine defects
    to assess project status
    used to provide historical record of software production
informal
formal
walkthroughs
formal reviews
inspections
audits

## Slide 22: V&V Techniques (con’t)
common V&V techniques
  formal review
  walkthrough
  inspection
  audit
Expected results: Know the purpose of the review. Know what is to be test or reviewed.
Responsibilities: Clearly assign responsibilities of all participants
Individual rights: Protect the opinions and feelings of individuals, not a committee
Attendees: The right people - some outsiders and some insiders
Structured process: Established procedures
Moderator: Skilled and trained
Records: Written report and evaluation
critical success factors

## Slide 23: Formal review
... is “a formal meeting at which a product or document is presented to the user, customer, or other interested parties for comment and approval.” (IEEE)
Objectives
  evaluate a specific software element and provide evidence that it satisfies specs and standards
  identify deviations from specifications and standards
Categories of formal reviews
  milestone
  technical
  managerial

## Slide 24: Formal review (con’t)
People
  Leader - facilitates meeting
  Scribe - documents findings
  Team members - present information, formulate recommendations
Review process
  plan
    identify conditions that must be complete before review is conducted
    identify conditions that must be met for the review to be completed
    identify records and documentation to be kept
    identify review team
    schedule and announce the meeting place
    distribute input materials

## Slide 25: Formal review (con’t)
Review process (con’t)
  conduct
    present overview of inputs to review (e.g., overview user needs at requirements review, etc.)
    discuss solution alternatives
    present selected alternative(s)
    receive endorsement/approval
    prepare review findings and report
  follow-up
    resolve any issues not resolved during review

## Slide 26: Formal review (con’t)
Common reviews
Software life
cycle
Develop-ment planning
System & s/w rqmt analysis
Prelim Detailed
design design
Code & unit
test
Intra-s/w integr testing
Req trace & perform
Inter-s/w Stress
integr test
testing
Operation &
Maintenance
* * * * * * * *
Baselines funct alloc developmental product deliv
* * * * * * * * *
Reviews SRR SDR SSR PDR CDR TRR FCA PCA FQT/AR
SRR System Req Review System Specification
SDR System Design Review System Design Document, (Software Requirements Specification), (Interface Requirements Specification)
SSR SW Spec Review Software Requirements Specification, Interface Requirements Specification
PDR Preliminary Design Review (Software Design Document), Software Test Plan, (Interface Design Document)
CDR Critical Design Review Software Design Document, Interface Design Document, (Software Test Description)
TRR Test Readiness Review Software Test Description
AR Acceptance Review All documents
Notes: might also have management review where Software Management Plan is reviewed and approved.

## Slide 27: Formal review (con’t)
Example -- PDR
  expected results
    approval of basic design approach/alternative selected
    acceptance of a preliminary design specification as the design baseline
    agreed-upon acceptance criteria for the critical design review
  process
    input
      preview packet containing participant checklists and review procedures
      review orientation session one week prior to start
      preview study of preliminary design specification and list of rejected design alternatives
Notes: example
  expected results
    criterion: signatures on design alternatives approval letter
    criterion: checklist scores above xxx
    criterion: signatures on design test plan

## Slide 28: Formal review (con’t)
Example -- PDR (con’t)
  process (con’t)
    procedure
      presentation and overview of functional specifications
      discussion of design alternatives considered (if “small” enough)
      review and approval of basic alternative selected
      presentation of preliminary design specification
      completion and scoring of review checklists
      presentation of design test plan
      preparation of review findings and report
    output
      decision endorsing design alternative selected
      formal review report including individual checklist scores
      approval of preliminary design specification and design test plan

## Slide 29: Walkthrough
... is a presentation review in which a review participant narrates a description of the software and the remainder of the review group provides their feedback throughout the presentation.
... is informal
... a.k.a. peer review
objectives
  detect, identify, and describe defects
  examine alternatives and stylistic issues
  provide a mechanism for authors to collect valuable feedback on their work, yet allows them to retain the decision-making authority for any changes
Notes: Walkthroughs can be viewed as presentation reviews in which a review participant, usually the developer of the software being reviewed, narrates a description of the software and the remainder of the review group provides their feedback throughout the presentation
These are referred to as presentation reviews because the bulk of the feedback usually only occurs for the material actually presented at the level it is presented.
Thus, advance preparation on the part of reviewers is often not detectable during a walkthrough.
Walkthroughs suffer from these limitation as well as the fact that they may lead to disorganized and uncontrolled reviews.

## Slide 30: Walkthrough (con’t)
People
  reviewer
  reviewing team
Timing: completion of specific milestones (e.g., completion of design for a module, etc.)
Process
  plan
    identify walkthrough team
    schedule time, place
    distribute materials in advance (if appropriate)

## Slide 31: Walkthrough (con’t)
Process (con’t)
  conduct
    overview item to be examined
    “walk through” item so that reviewers may understand and ask questions
    write walkthrough report
      identification of walkthrough team
      identification of item reviewed
      statement of objectives of walkthrough
      list of noted deficiencies, omissions, contradictions, suggestions
      recommendations made by reviewers on how to disposition deficiencies
Implementation challenges
  find, don’t fix
  ego
  organization

## Slide 32: Audits
... is a “review of the project to assess compliance with software requirements, specification, baselines, standards, procedures, codes, and contractual and licensing requirements.” (IEEE)
common V&V audit:
  function configuration audit (validates conformance to requirements)

## Slide 33: Inspection
... is “a formal evaluation technique in which software requirements, design, or code are examined in detail by a person or group other than the author to detect faults, violations of development standards, and other problems.” (IBM)
objective:
  detect, identify, and describe defects
  collect software engineering data (e.g., defect and effort data)
  verify the software element’s “fitness for use” in subsequent efforts
  provide a control mechanism that determines the next process step
Notes: definition
common inspections: the inspection depends on the material being examined. Personnel attending inspection will vary depending on the material being inspected.

## Slide 34: Inspection (con’t)
Essential requirements
  definition of development process in terms of operations and their exit criteria
  proper description of the inspection process
  correct execution of the inspection process
Common inspections:
  High-level design inspection (I0)
  Low-level design inspection (I1)
  Code inspection (I2)
Notes: essential requirements
  def of dev process
    operations: what actions have been taken to produce the product to be inspected
    exit criteria: standards against which inspections measure the completion of a product at the end of an operation. e.g.,
      clean compile
      requirements/design changes included
      all rework from previous inspections included
      output of operation preceding current operation complete
common inspections: determines inspection team, materials to examine, focus of inspection

## Slide 35: Inspection (con’t)
Participants
  moderator (facilitates meeting)
  author (designer or coder)
  reader (paraphrases design or code)
  tester (views module from testing standpoint)
  others (as needed)
moderator
author
related area
scribe
tester
reader
checklist

## Slide 36: Inspection (con’t)
Participants (con’t)
  moderator
    prior to inspection
      be trained
      determine whether entry criteria for inspection has been met
      work with author to establish team membership
      preview material for conformance to standards
      ensure team size and mix is appropriate
      establish inspection time, place
      ensure materials are distributed
    during the inspection
      ensure adequate attendance
      ensure adequate preparation; if not, postpone
      facilitate inspection meeting
      log defects
      require reinspection of major defects
    after the inspection
      review results with author
      provide manager with estimate of rework completion data
      write inspection summary and distribute

## Slide 37: Inspection (con’t)
Participants (con’t)
  Author
    prior to inspection
      prepare material to address al inspection level checklist items
      review material with moderator for completeness
      provide summary information
        major function, major points of interest, estimated vs actual: SLOC, resource utilization
      produce materials distribution package
    during the inspection
      answer questions
    after the inspection
      complete all rework required
      verify fixes will correct problem and not cause side effects
      verify to moderator that changes have been made

## Slide 38: Inspection (con’t)
Participants (con’t)
  Reader
    prior to inspection
      review material
    during the inspection
      guide inspection team through material during meeting; paraphrase or verbalize the review material
      present material with clarity and understanding
      note any items difficult to understand
      be able to tie back to specification or design
    after the inspection
      assist in verifying follow-up items have been completed
  Tester
    must determine whether inspected item can be verified
    must ensure that code is compatible within the system
    must understand verification practices and enforce them

## Slide 39: Inspection (con’t)
Process
  planning
    ensure materials meet inspection criteria
    arrange availability of participants
    arrange suitable time and place
  overview
    educate participants on what is to be inspected
    assign inspection roles
  preparation
    participants learn material and prepare to fulfill assigned roles

## Slide 40: Inspection (con’t)
Process (con’t)
  inspection
    introduce participants and verify preparedness
    review software and record defects
    review defect list
    make exit decision
      accept: software element accepted “as is” or with minor rework. Reinspection not required
      verify rework: software element is to be accepted after the moderator verifies rework
      re-inspect: schedule inspection to examine reworked software element
  rework
    author addresses all defects
  follow-up
    verify all fixes are effective and haven’t introduced secondary defects

## Slide 41: Inspection (con’t)
Inspection challenges
  training in psychology of inspections
  making inspections impersonal
  inspections limited to small groups of peers
  consistent data collection
  use of inspection data
Notes: inspection challenges
  training: programmers must be trained in the psychology of inspections. Must develop an atmosphere of egoless review of code
  impersonal: inspection reports must not criticize individuals. Information should be provided to the management team so that proper decisions can be made, yet it must be done in such a way that any individual programmer will not feel intimidated or degraded.
  small groups: avoid hordes
  consistent collection of data: standard (agreed-upon) metrics must be collected
  use of inspection data: management must not use data to evaluate individual performance, but to guide quality.

## Slide 42: Comparison
 | Formal Review | Inspection | Walkthrough
Objective | Established in stmt of objectives | Detect and identify defects | Detect defects; examine alternatives
Decision-making | Review team petitions mgmt/technical leader to act on recommendations | Team chooses from predefined categories: defects must be removed | All decisions made by author; change is prerogative of author
Change verification | Leader verifies as part of review report | Moderator verifies rework | Accomplished through project controls
The team | Technical leadership and peer mix; >3 people; leader is principle engineer; presenter represents development area | 3-6 peers meet with documented attendance; leader is trained moderator | Technical leadership and peer mix; 2-7 people; leader is usually author
Material volume | Moderate to high | Relatively low | Relatively low
Data Collection | Not a formal project requirement | Formally required; defects counts, severity, meeting attributes kept | Not a formal requirement

## Slide 43: Assessing effectiveness
Error detection efficiency
  ratio of defects detected by review process to the number of defects detectable
Error cost effectiveness
  ratio of costs saved by the review process to the actual cost of the process
Error seeding
  intentional introduction of errors to evaluate error detection
Notes: error detection efficiency: By examining error rates over a statistically significant period of time, we can predict roughly how many errors appear in a product at various points in the life cycle. We can then use actual number of errors detected after the fact.
error cost effectiveness: ration of costs saved by the review process to the actual cost of the process. The actual cost of a review process can be measured several ways, typically using some variation of manhours. The costs saved by a review is much harder to quantify and usually requires a statistical analysis of the errors detected by the review, where these errors may have been detected if the review was not held and the cost associated with fixing the error at a later stage then if it was caught by the review.

## Slide 44: Summary
Topics
First principles
  rationale
  role
Organizational activities
V&V approaches
  Formal review
  Walkthrough
  Audit
  Inspection
Assessing effectiveness
Key Points
V&V addresses requirements congruency
V&V deals mostly with non-executable items, happens at all lifecycle activities
Primary V&V techniques: walkthroughs, formal reviews, audits, inspections